## Slide 1: Transducers & Instrumentation
Module 04
Measuring Forces and Torques

## Slide 2: Forces and Torques
Forces and torques cause bodies to undergo linear or rotational acceleration.
Cause deformation.

## Slide 3: Resistance of a material
Piezoresistivity
Geometric factor
Gauge factor
Strain

## Slide 4: Gauge factors of common metals
Material | Sensitivity ()
Platinum (Pt 100%) | 6.1
Platinum-Iridium (Pt 95%, Ir 5%) | 5.1
Platinum-Tungsten (Pt 92%, W 8%) | 4.0
Isoelastic (Fe 55.5%, Ni 36% Cr 8%, Mn 0.5%) * | 3.6
Constantan / Advance / Copel (Ni 45%, Cu 55%) * | 2.1
Nichrome V (Ni 80%, Cr 20%) * | 2.1
Karma (Ni 74%, Cr 20%, Al 3%, Fe 3%) * | 2.0
Armour D (Fe 70%, Cr 20%, Al 10%) * | 2.0
Monel (Ni 67%, Cu 33%) * | 1.9
Manganin (Cu 84%, Mn 12%, Ni 4%) * | 0.47
Nickel (Ni 100%) | -12.1
Material | 
Platinum (Pt 100%) | 6.1
Platinum-Iridium (Pt 95%, Ir 5%) | 5.1
Platinum-Tungsten (Pt 92%, W 8%) | 4.0
Isoelastic (Fe 55.5%, Ni 36% Cr 8%, Mn 0.5%) * | 3.6
Constantan / Advance / Copel (Ni 45%, Cu 55%) * | 2.1
Nichrome V (Ni 80%, Cr 20%) * | 2.1
Karma (Ni 74%, Cr 20%, Al 3%, Fe 3%) * | 2.0
Armour D (Fe 70%, Cr 20%, Al 10%) * | 2.0
Monel (Ni 67%, Cu 33%) * | 1.9
Manganin (Cu 84%, Mn 12%, Ni 4%) * | 0.47
Nickel (Ni 100%) | -12.1
Source: https://www.efunda.com/designstandards/sensors/strain_gages/strain_gage_sensitivity.cfm

## Slide 5: Strain gauges
Sensitive to length changes along this direction.
Strain gauge made from metal foil.
Strain gauge bonded to a cantilever.
Backing film
Source: https://resourcespace-prod.s3.amazonaws.com/rs/filestore/1/1/6/3/9_981464e59f794c3/116391ai_b5fc4cbf03762f5.jpg
Source: https://5.imimg.com/data5/BG/MR/MY-41643329/strain-gauge-500x500.jpg

## Slide 6: Strain gauges
Sensitive to length changes along this direction.
Strain gauge with GF 2.5 and resistance 150 ohms.
Problem:
Experiences a 400 micro-strain
What is the change in resistance of the strain gauge?
Source: https://5.imimg.com/data5/BG/MR/MY-41643329/strain-gauge-500x500.jpg

## Slide 7: Measuring resistance change of strain gauges
Wheatstone Bridge
The bridge is balanced when, .

## Slide 8: Wheatstone bridge with a single strain gauge
Let’s assume changes by

## Slide 9: Wheatstone bridge with a single strain gauge

## Slide 10: Bridge Constant & Calibration Constant

## Slide 11: Some load-cell configurations
Cantilever based load-cell
Single strain gauge
Double strain gauges
Four strain gauges

## Slide 12: Some load-cell configurations
Tension/compression load-cell
4
1
3
2
4
1
3
2

## Slide 13: Strain gauge torque sensors
Directions of maximum tensile stresses.
1
4
4
2
Torque computed from

## Slide 14: Semiconductor strain gauges
Highly sensitive to small strains compared to metallic foil strain gauges.
Change of resistivity due to a mechanical strain: Piezo-resistivity.
Gauge factor: 100 to 170 for p-type Silicon, -140 to -100 for n-type Silicon.
Higher resistivity, lower power consumption, lower heat dissipation.
Metal foil strain gauge: 150-350 ohms, SC strain gauge: 5000 ohms

## Slide 15: Semiconductor strain gauges
Some disadvantages:
  Non-linear strain-resistance relationship.
  Brittle and difficult to mount on curved surfaces.
  Max. measurable strain is an order of magnitude lower.
  Costly
  More sensitive to temperature.
Normalized resistance change of SC strain gauges:
Source: De Silva, C W, Sensors and Actuators, CRC Press (2007)

## Slide 16: Temperature compensation

## Slide 17: Temperature compensation
Resistance of materials are sensitive to temperature.
Resistivity changes with temperature.
This linear approximation works when .
Semiconductor strain gauges are more sensitive than metal foil strain gauges.
For semiconductor strain gauges the resistance change is larger, and the gauge factor is also temperature dependent.